## Slide 1: Lee’s Wire Routing Algorithm

## Slide 2: Application of Queue: Wire Routing
Select paths to connect all pairs of pins that need to be connected together.
An important problem in electronic design automation.

## Slide 3: A Simplified Problem
Condition: We have all blocks laid on the chip. We also have some of the wires routed.
Problem: We want to connect the next pair of pins.
Constraint: we can only draw wires horizontally or vertically.
Start Pin
End Pin

## Slide 4: Modeling as a Grid
Start Pin
End Pin
Blue squares are blocked squares.
Orange squares are available to route a wire.
How to find a path from the start pin to the end pin?

## Slide 5: Wire Routing: Lee’s Algorithm
A queue of reachable squares from the start pin is used.
The cell of the start pin is set with a distance value of 0.
It is enqueued into an initial empty queue.
While the queue is not empty.
  A cell is dequeued from the queue and made the examine cell.
  Is the examine cell the end pin? If yes, path found and return.
  Otherwise, all unreached unblocked squares adjacent to the examine cell are marked with their distance (this is 1 more than the distance value of the examine cell) and enqueued.
When queue becomes empty but not reach end pin yet, means no path found.

## Slide 6: Illustration of Lee’s Algorithm
start pin
end pin
Expand “0”
1
1
0
queue: 0

## Slide 7: Illustration of Lee’s Algorithm
start pin
end pin
Expand right “1”
1
1
0
queue: 1, 1
2
2
2
Notes: Now the queue becomes 1,1, since 0 is removed and two 1’s are added.

## Slide 8: Illustration of Lee’s Algorithm
start pin
end pin
Expand left “1”
1
1
0
queue: 1,2,2,2
2
2
2
2
2
Notes: Now the queue becomes 1,2,2,2.

## Slide 9: Illustration of Lee’s Algorithm
start pin
end pin
Expand and reach all squares 3 units from start.
1
1
2
2
2
2
2
0
Notes: It is like expand and reach all squares 2 units from start.

## Slide 10: Illustration of Lee’s Algorithm
start pin
end pin
Expand and reach all squares 4 units from start.
1
1
2
2
2
2
2
3
3
3
3
0

## Slide 11: Illustration of Lee’s Algorithm
start pin
end pin
Expand and reach all squares 5 units from start.
1
1
2
2
2
2
2
3
3
3
3
4
4
4
4
4
0

## Slide 12: Illustration of Lee’s Algorithm
start pin
end pin
Expand and reach all squares 6 units from start.
1
1
2
2
2
2
2
3
3
3
3
4
4
4
4
4
5
5
5
5
5
5
0

## Slide 13: Illustration of Lee’s Algorithm
start pin
end pin
End pin reached. Trace back.
1
1
2
2
2
2
2
3
3
3
3
4
4
4
4
4
5
5
5
5
5
5
6
6
6
6
6
6
6
0
6

## Slide 14: Illustration of Lee’s Algorithm
start pin
end pin
4
1
1
2
2
2
2
2
3
3
3
3
4
4
4
4
4
5
5
5
5
5
5
6
6
6
6
6
6
6
3
5
2
1
0